TC-809 Artnet Controller

## 1.Peoduct Introduction

## The TC-809 controller is a controller with LCD digital interface display, which converts Art-Net signals into various pixel lamp chip signals. It adopts standard Ethernet transmission and also accepts DMX512 signal control. Eight output ports, can control a variety of LED driver chips, support automatic addressing function, convenient for users to access different types of lamps, and realize unified control of different lamps in the project. The input network port can be directly connected to the computer network card, and can also be connected to the computer network card via a switch or photoelectric converter. It is widely used in buildings, municipal lighting, stage scenery, entertainment venue decoration, etc.; it can achieve various running changes such as horse racing, running water, tailing, color painting, scanning, raindrops, etc., and has the advantages of convenient wiring and simple use; Single unit can also be used in cascade connection.

## 1)Techinical Parameter

|  | Specification |
| --- | --- |
| Voltage: | DC5～24V |
| Input signal: | ArtNet / DMX512 |
| Output signal: | 8 X TTL / RS-485 |
| Frame: | 30（ms） |
| Control Pixels: | RGB：1020pixel×8CH / RGBW：765pixel×8CH |
| Cascade QTY： | 128台：170pixel×8CH / 64台：340pixel×8CH / 42台：510pixel×8CH / 32台：680pixel×8CH / 25台：850pixel×8CH / 21台：1020pixel×8CH |
| Working temperature: | -20~55℃ |
| IP grade: | IP20 |
| Accessories: | 8G SD card / Green 3Pin connector * 8 / Green 2Pin connector * 1 |
| Size: | L180 * W138 * H29(mm) |
| Weight: | 380g |

2)Function and Features.

.1. Provide LCD liquid crystal screen display, which can display the model, ID, and working status of the controller.

2.8 output ports, each port can load up to 170/340/510/680/850/1020 pixels (the number of load points varies according to different loaded chips).

3. Two signal protocols for port output: ①DMX512/1990 international standard protocol and DMX512 extended protocol (RS-485 differential signal); ②TTL serial protocol (level signal).

4. Support a variety of pixel control IC, flexible control method

5. Controller network IP online/manual setting function.

6. With DMX512 address writing function, single port or all ports load DMX512 IC address writing.

7. It can be directly connected to the computer network card when online, or it can be connected to the computer network card through a switch or photoelectric converter.

8. It can be used as a single unit, or multiple units can be cascaded to use, and supports multi-channel connection of switches.

9.Support DMX512, online and offline integrated control, online priority is the highest, automatically switch to offline playback when there is no 2 online and DMX51 signal, online can be connected to Madrix, offline can be connected to DMX512 console.

10. The SD card stores offline effect files and supports the download of effect files via ArtNet network, without the need to insert or pull out the SD card.

11. Flexible use when online, it can be used as the main control (insert SD card), and can also be used as a sub-controller (without SD card).

12. Sub-control cascade, can be interchanged arbitrarily, and has strong adaptability to lighting engineering.

13. The communication adopts the international standard TCP/IP network protocol, the optional transmission rate supports 100M/Gigabit adaptive, the transmission speed is more stable and fast, and the nominal transmission distance between each two controllers can reach 100 meters.

14. The network interface with indicator light is adopted, the working status is clear at a glance, and the T568B line sequence protocol is adopted.

15. Port ESD protection design,

16. Power input interface reverse connection protection design

3)Use Precautions

1. To ensure safety and normal use of the product, please read the instruction manual carefully before use.

2. Try to avoid minefields, strong magnetic fields and high voltage areas during installation.

3. Ensure that the wiring is correct and firm, so as to avoid short-circuit damage to components and trigger fire accidents.

4. Please install the controller in a well-ventilated place to ensure proper ambient temperature.

5. The controller must be equipped with a DC constant voltage switching power supply. Please check whether the input power supply meets the product requirements and whether the output voltage of the power supply is consistent with the product before turning on the power.

6. Live wiring is forbidden. After checking that the wiring is correct, check that there is no short circuit, and then turn on the power again!

7. Please do not repair it privately in the event of a fault. If you have any questions, please contact the supplier.

## 2. Product Details

Unit：mm

1)Details of the controllers

|  | Item | Function |
| --- | --- | --- |
| 1 | Power input | DC5～24V input |
| 2 | DMX A/B port | DMX signal port(A input, B output) |
| 3 | Red light | Power indication |
| 4 | Green light | DMX signal work (Flash) |
| 5 | SD card groove | Insert SD card |
| 6 | Network green ligt | Network work (Keep shining) |
| 7 | Network yellow light | Network work ( flash） |
| 8 | LINK-IN/OUT | ArtNet signal (Input，Output) |
| 9 | Buttons | Setting parameters |
| 10 | Led screen | Display the informaation of controller |
| 11 | Output connectors | Connect to led products |

2)Silkprint details.

| Silkprint | Function |
| --- | --- |
| DC 5～24V | Power input |
| DMX A / DMX B | DMX signal port(A input, B output) |
| POWRE/ACTIVE | Power indication light |
| SD CARD | SD card groove |
| NET_IN/NET_OUT | Ethernet signal input and output |
| MENU － + ENTER | Buttons |
| OUT-1 OUT-2 OUT-3 OUT-4 OUT-5 OUT-6 OUT-7 OUT-8 | 8 output for led products |
| A GND B/DO | Wire define |

3)Operating Instructions

1.Output details：

When outputting DMX512/HDMX/TM512/UCS512/SM16512 control signals (differential), three wires are required. When outputting control signals (TTL) such as WS2811/TM1804/UCS1903/GS8206, two wires are required. The wiring method :：

| Define | RJ485 Signal wire | TTL Signal |
| --- | --- | --- |
| A | （D+） |  |
| B/DO | （D-） | DATA |
| GND | GND | GND |

2.Control IC chips:

| IC Type | IC chips | Color |
| --- | --- | --- |
| 2811 | TM1804、TM1809、TM1812、UCS1903、UCS1909、UCS1912、UCS2903、UCS2909、UCS2912、UCS2919、WS2811、WS2812、GS8206 etc. | RGB |
| 1914 | TM1914 |  |
| 5603 | UCS5603,etc. |  |
| 512 | DMX512、HDMX、TM512、UCS512、SM16512 etc. |  |
| 2904 | UCS2904B etc. | RGBW |

- Software instructions:

- Open the software

Click the "Search Controller" button, when the controller is searched, then set the parameters of the controller .

- Before Set the IP address and parameters we need to know:

|  | Details | Precautions |
| --- | --- | --- |
| IP address | Distinguish each network device in the local area network | Must be on the same network segment as the computer |
| Subnet mask | IP is divided into network address and host address | Must be the same as the computer settings |
| Number of cascade sub-controllers | Number of connectable sub-controllers |  |
| Starting space | Virtual space in the first output port MADRIX software |  |
| Chip type | Loaded IC signal output by port | Must be the same as the on-board IC signal protocol on the connected luminaire |
| Port loaded pixels | The number of pixels that can be controlled by the controller output port | Connect the port with the most pixels |
| Port mode | 8 or 4 ports have light control signal output | When set to "4", there is no signal output from the "6-8" ports of each controller |

- Set the IP address.

Double-click the corresponding number box, after the number is selected, you can change it as needed, and set the controller's IP address, sub-control number, starting space, etc.

Note: The above is the grouping of the controller to the switch. When the controller is directly connected to the computer, only one IP address will appear.

- Choose the IC chip.

- Choose the Port qty and the Pixels loaded.

- Choose the Port type

- MAC address

When the controller is connected to the LAN and conflicts with the MAC address of other devices in the LAN, click the number in the "New MAC Address" box. After the number is selected, you can change it as needed. After setting each parameter, click "Send to Controller" to save the parameters to the controller.

- Testing status

In the "Test Mode" functional area, select the current controller port number according to the actual application, check the output port to be tested, select the current controller port to be loaded, fill in the IP address and serial number of the controller to be tested, and Fill in the location of the pixel to be tested on the port, set the light-emitting color of the test point, click "start test", and the pixel on the side of the position will light up the corresponding light color. If the test pixel position or light color is changed, the position of the lit pixel and the light color emitted will also change in real time. In the same way, changing the IP address, serial number value, and changing the port selection will also cause the location of the test pixel to change.

Note: When the controller only uses 4 ports, "Port 5" to "Port 8" are not selectable

- Controllers IP grade and serial number.

- One-key address writing function for DMX512 lamps

Channel interval input

The channel interval is according to the actual digital input of the lamp, and the number is the number of channels occupied by a DMX512 IC to control the pixel of the lamp. For example: 8-segment full-color LED linear light, each segment occupies 3 channels, then 3*8=24, that is, the channel interval is "24".

Start channel input

The default starting channel is "1", when you need to change it, press the actual input number.

Confirm that the settings are correct, and click "Write Address" to complete the program output.

## 4.Working with Madrix

- MADRIX

- Connect to Madrix

Run the "MADRIX" software, click "Preferences", select Device Manager from the drop-down menu or press the "F4" key to pop up the Device Manager menu, and select the "Art-Net" tab.

- Art-Net Setting

. Select the "Art-Net" tab, check the "Enable" checkbox in the upper right corner, click the search button to search for the port of the controller, and click "Apply" below to enable Ethernet output.

Select "ArtNET Remote" and click "Sync" in the upper right corner. In the pop-up "Sync Mode" dialog box, double-click the IP option of the same network segment as the controller to open the synchronization, and set the "Before synchronization" and " After synchronizing, click on the two checkboxes,

Click "OK" below to activate "Sync". And return to the device management interface..

Click the“ArtNET Remote”and change the IP address into“127.0.0.1”。

- DMX devices setting.

select the "DMX Devices" tab, select all devices, activate the "Enable" check box on the right, and click "Apply" below to enable DMX output

- DMX输入设置

Choose“DMX输入”，and the“1”的chart，find the ArtNet Remote (MADRIX) Port:0”。

。

## 5.Use precautions.

1.SD Card formatting

1. Before copying files to the SD card, the SD card must be formatted (note that it must be formatted before each copy)

2. Formatter

① SD card settings—"File system", "FAT" format (SD card capacity≤2G) or "FAT32" format (SD card capacity≧4G).

②SD card settings—"allocation unit size", click the drop-down button to select "32K".

③Start formatting.

The SD card on the controller cannot be hot-plugged, that is, every time the SD card is inserted or removed, the controller must be disconnected from the power supply.。

2.File Naming

1) The effect program file is named with a number at the beginning, and the number cannot exceed 3 characters, otherwise it may cause SD card file errors. When the file name needs to be described in text, the number and the text must be separated with an underscore "_"。：

2)When multiple effect program files are stored in the SD card, each file name must start from "000" and be named in an increasing manner of "001, 002, 003...010, 011...". There must be no missing in the middle。

3.Online cascade

4.Offline cascade

5..After-sale Services

From the date of purchase of this product, if quality problems occur during normal use according to the operating instructions within 3 years, the company will provide free repair or replacement services.

If the product is damaged due to failure to follow the instructions in this manual and the following terms, the company is not responsible for any problems and defects caused by this, even during the warranty period,

Maintenance costs must also be borne by the customer.

1. Damage caused by misoperation, such as misoperation not in accordance with the operating instructions.

2. Damage caused by improper power supply and excessive voltage.

3. Damage caused by unauthorized removal, repair, circuit modification, incorrect connection, and unauthorized replacement of chips.

4. Damage caused by transportation, shock, falling, and water after purchase.

5. Damage caused by earthquakes, fires, floods, lightning strikes, natural disasters, and environmental pollution.

6. Damage caused by improper maintenance such as storage in a high temperature and humid environment, away from harmful chemical