In order to allow you better and more convenient and quick construction in the engineering installation, please read this manual carefully before installation, if you have any questions, please call and understand clearly before construction.

- Accessories：

The firework tree is mainly composed of light tubes, main structure, light bars, speakers, and controllers. Just follow the steps when installing!

2.、Steps：

1)Take out various accessories, check whether the circuit is off, whether the structure is damaged, and if there is no abnormality。

1）install the 15mm led tube：

The led tube is fixed on the inside and outside by two nuts, tighten it! !

(Two open-end wrenches are provided with the box)

2）Connect the wires：

The connector on the lamp tube is connected with the internal T-connector

Take the nearest connection, pay attention to align the gap

inside the terminal when inserting, Screw the caps tightly after connection. total of 16 groups! !

- Connect the tube with 3D diamond led strings：

- The diamond lamp is used to fix it on the pole, and

the male connector is Below, the female connector is on the

upper part, the female connectorand the T- connector head

Totally of 3 groups!

- Connect to the controller

Connect to the 3D diamond led string

Audio signal output connector

- Connect to the Speaker

Audio connector from the controller                                         DC wire to connect to power supply  Speakers must beConnected Upper wire color interface！）

Button to adjust the voice

The speakers need to be installed vertically, and the wiring part faces downwards, which is very important!

- Controller.

1. By default, the controller is set according to the number of light bars and tube points shipped. If you increase or decrease the number of light bars during the actual installation process, you need to reset the controller

2.The connection line of the controller is the main body of the controller, if it is used outdoors, it needs to be waterproofed separately.

3.Setting method: This is the remote control of the controller, please observe the indicator light on the controller when setting! Refer to the following method

MODE             +               -        ON/OFF

MODE：1. For the first time, long press 3 seconds to enter the point setting of the first segment (led strip), the indicator light is red, press +-key to adjust the points

- Press and hold 3S for the second time to enter the point setting of the second segment (diamond string), the indicator light will be green, press +-key to adjust the point

- Long press 3S for the third time to enter the speed setting of the first segment (led strip), the indicator light flashes red, press +-key to adjust the speed

- Press and hold 3S for the fourth time to enter the speed setting of the second segment (3D diamond string), the indicator light flashes green, press +-key to adjust the speed

- Press and hold 3S for the fifth time to exit the setting mode

“+”button：You can increase the number of points when setting the status (note: the total number of points cannot exceed 512), or increase the speed of the running effect

“-”button：The number of points can be reduced when setting the status (note: the total number of points cannot exceed 512), or the running effect speed can be reduced

ON/OFF button：Sound source used to turn speakers on and off

U shape lock

- Cable reel installtion

The base of the wire reel and the light pole

adopt the matching U Type screw lock

- Install the power supply

Fix it on the light pole with

a screw rod as shown in the figure,

Note that the wiring is facing down

and the power supply is vertical

Installation status

4wires from the reel connect to power supply.

(White edge wire for DC12V+,DC12V- with GND).

DC wire  for the speaker

AC220V   4 wires from reel   for speaker

- Connect the tube

3.．Precautions

1、During operation, check that all connectors are not missing or incorrectly connected before powering on.

2、The input voltage of the controller is DC12V, please note that the voltage cannot be connected wrongly, otherwise the controller will be burnt out.

# Text boxes

The other four M4 rods are used to adjust the balance of the two rods

The thin tube is the upper part, the thick tube is the lower part,

and the thin tubeSleeve into the thick tube and use two long screw

rods to pass out,Lock the cap